## Slide 1
Flows Move Primarily Along the Helical Direction of Symmetry
Geometric factors are used to relate the measured velocities to the average flow in the symmetry and cross symmetry directions within the view
Near the axis the flow direction change significantly across the beam/view volume
Neutral Beam
Typical
Poloidal
View
Volume
“Toroidal” Views
“Poloidal” Views
Velocity Measured By Each View
Velocity Along and Across the Symmetry Direction

## Slide 2
30keV, 4Amp, 3ms hydrogen neutral beam is fired radially
C+6 ions charge exchange with the neutral beam
529nm light from the C+5 ions is collected
Two 0.75m imaging Czerny-Turner spectrometers with electron multiplying ccds image the spectra
Frames integrated for 5ms are taken before, during and after the beam fires
Charge Exchange Recombination Spectroscopy (CHERS) On HSX
Neutral
Beam
Density
“Poloidal”
Views
Neutral Beam
“Toroidal”
Views
Neutral Beam
“Toroidal”
Views
“Poloidal”
Views

## Slide 3
DKES predicts ~0 V|| for all values of Er because it does not account for momentum conservation in collisions
V|| is Determined by and Viscosity
V┴
V
V||
ζBoozer
|B| and Velocity in HSX
θBoozer
B
PENTA
DKES
Helical Flow

## Slide 4
nC+6
nH+
The Measured Density and Temperature Profiles Input to PENTA
Te and ne measured using Thomson Scattering
Ions are collisional and have the same temperature and V||
Te
60eV>TC+6>30eV
TH+=TC+6
ne

## Slide 5
PENTA predicts a small positive Er at the edge
Differences between the Er predicted by PENTA and DKES become significant when there are multiple ion species in the calculations
Agreement Seen Between Measured Er and The PENTA Value
Measured and Calculated Er
Measured
DKES
PENTA

## Slide 6
DKES under-predicts V|| by more than an order of magnitude
Better agreement is seen with the PENTA code which accounts for momentum conservation
Flows Predicted PENTA, Including Momentum Conservation Show better Agreement
PENTA
Measured
DKES
Measured and Calculated V||

## Slide 7: Measurement and Modeling of Large Helical Flows in the HSX Stellarator
Alexis Briesemeister
HSX Plasma Laboratory
Electrical & Computer Engineering, UW-Madison
54th Annual Meeting of the APS-DPP, Providence, Rhode Island October 31, 2012

## Slide 8: Motivation
Quasi-symmetry allows large intrinsic flows in stellarators, which typically have large flow damping
  HSX was optimized for quasi-helical symmetry
Flows improve plasma confinement and stability
  Using neutral beams to drive flows is impractical for larger devices, intrinsic flows become important
This is the first test of the PENTA code which can calculate intrinsic flows in devices with any level of symmetry
  Non-symmetric fields can increase flow drive, but damp plasma rotation

## Slide 9: Outline
The quasi-symmetric HSX stellarator
  Charge exchange recombination spectroscopy (CHERS) used to measure flow speed and direction
  Flows move in the helical direction with speed 20km/s
PENTA code is used to calculate neoclassical transport, Er and parallel flow
  The ambipolar constraint determines Er in configurations with significant non-symmetric field components
  Includes momentum conservation and multiple ion species
Measured and predicted flows agree only when momentum conservation is accounted for

## Slide 10: The Quasi-Helically Symmetric HSX Stellarator
Quasihelical symmetry (QHS) reduces neoclassical transport [Canik PRL, 2007] and flow damping in the helical direction [Gerhardt PRL, 2005]
QHS
N=4, m=1
  1
eff = |N-m|  3
<R> | 1.2 m
<a> | 0.12 m
 | 1.05 1.12
B0 | 1.0 T
ECRH 28 GHz | 100 kW
<ne> |  6  1012 cm-3
Te | 0.5 to 2.5 keV
Ti | 30 to 60 eV
no external momentum source, all flows shown are intrinsic

## Slide 11
The Total Flow has Perpendicular and Parallel Components
Er is determined by neoclassical transport
Diamagnetic flow small for higher Z ions like carbon
VPS is the Pfirsch-Schlüter flow that varies on a surface, causes the total flow to satisfy incompressibility
All flow components change direction if is reversed
  Using the flow reversal with eliminates error from uncertainty in the unshifted line position

## Slide 12
Electron impact ionization, recombination, and charge exchange are included [ADAS: Summers (2004) ]
No measurement of all ionizations states is currently available
Carbon to hydrogen ratio taken to be 1 to 4, methane
Coronal Equilibrium Used to Find Abundance of Other Carbon Ionization States

## Slide 13
The DKES (Drift Kinetic Equation Solver) code [Hirshman PoF 1986] is used to find the mono-energetic diffusion coefficients
  Uses a non-momentum conserving collision operator
  Developed for conventional stellarators with large flow damping
The PENTA code[Spong PoP 2005] corrects the mono-energetic diffusion coefficients from DKES for momentum exchange
  This correction makes PENTA valid for devices with any level of symmetry from ideal tokamaks to conventional stellarators
  Can include multiple ion species
Neoclassical Particle Flux and Flows are Calculated using the PENTA Code

## Slide 14
Electron’s Are in the 1/nu Regime In The Core
The hotter electrons are in the 1/n regime
Their flux peaks at Er=0
Γe
Particle Flux
Particle Diffusion
[Lore Thesis 2010]

## Slide 15
Multiple Roots are Predicted As a Result of the Helical Proton Resonance
Er is found by enforcing ambipolarity
Multiple roots of the ambipolarity condition are predicted in the core because of a peak in the ΓH+ near the helical proton resonance
Γe
Γi Total
Particle Flux

## Slide 16
driven by ExB and diamagnetic flows
V|| proportional to will arise to cause the total flow to move along HSX’s helical direction of symmetry
V|| is Determined by and Viscosity
V┴
V
V||
ζBoozer
|B| and Velocity in HSX
θBoozer
B

## Slide 17
With all else held constant, V|| should increase linearly with Er to cause the to total flow to move along the helical direction of symmetry
V|| is Determined by and Viscosity
V┴
V
V||
ζBoozer
|B| and Velocity in HSX
θBoozer
B
Helical Flow

## Slide 18
For small (ion root) values of Er PENTA predicts the protons will move in the direction of symmetry
Large values of Er detrap the particles responsible for the plasma viscosity, reducing V||
V|| is Determined by and Viscosity
V┴
V
V||
ζBoozer
|B| and Velocity in HSX
θBoozer
B
PENTA
Helical Flow

## Slide 19
The intrinsic plasma flow follows HSX’s helical direction of symmetry
Reasonable agreement between the measured and calculated flow is only seen when the effects of momentum conservation are included in the calculation
PENTA successfully predicts flows in a system that is largely symmetric
Conclusion

## Slide 20
Multiple Roots are Predicted As a Result of the Helical Proton Resonance
Er is found by enforcing ambipolarity
Multiple roots of the ambipolarity condition are predicted because of a peak in the ΓH+ near the helical proton resonance
Γe
Γi Total
Particle Flux

## Slide 21
Multiple Roots are Predicted As a Result of the Helical Proton Resonance
Electron root: Larger positive Er associated with reduced neoclassical transport
Ion root: Smaller, sometimes negative Er
Unstable root: Not a stable solution
Calculated Er Profile
Γe
Γi Total
Particle Flux
Electron root
Unstable root
Ion root

## Slide 22
HSX’s quasi-helical symmetry allows large flows to develop
The DKES (Drift Kinetic Equation Solver) code uses a non-momentum conserving collision operator
The parallel momentum conserving moments method techniques developed by Sugama and Nishimura[PoP 2002], and Maasberg, Beidler, and Turkin [PoP 2009] and Taguchi[Phys. Fluids 1992] were implemented by Spong and Lore in the PENTA code [Spong 2005] to correct the DKES coefficients
These techniques are valid for devices with any level of effective ripple, from tokamaks to conventional stellarators
PENTA Accounts for Momentum Conservation

## Slide 23
The charge exchange cross section used to find the C+6 density and the fine structure of the line used to correct the line width is taken from the Atomic Data Analysis Structure ADAS [Summers 2004]
Reversing the magnetic field reverses the flows, doubling the measured Doppler shift
Spectral calibration performed each shot to account for instrumental drift using a Neon lamp
Atomic Data and Field Reversal Used To Find Density, Temperature and Velocity
Fine Structure Broadening Comparable to Thermal Broadening
~0.04nm
Doppler shift is determined by flow velocity along the viewing direction
Thermal motion of the ion causes Doppler broadening of the spectral line

## Slide 24
PENTA calculates : and
where
The local flow is calculated on a grid of points throughout the beam/view intersection volumes:
Local Flow Velocity Can Be Calculated from PENTA Profiles and Magnetic Geometry
Gps =geometry factor for the Pfirsch-Schlüter flow
The calculated neutral beam density is used to create a weighted average of the velocity that would be “seen” by each view

## Slide 25: Including All Ions
Lines are old calculations with just protons and C+6

## Slide 26: Solving the Diffusion Equation for Er
1) Shaing (1984), Maassberg et al (1993). 2) Hastings (1985, 1986)
The radial electric field profile can be determined by solving a diffusion equation1
DE (related to perpendicular viscosity) is generally not known2
  Solutions for different DE show a region of strong Er shear at r/a~0.25
I stole this from J. Lore’s Dissertation, Do we now have a better calculation for DE?

## Slide 27
The CHERS system can only measure a weighted average of the local plasma flow within each beam/view intersection volume
The measured flows are much smaller (~20km/s) than the flows predicted by PENTA (~50 to 100km/s) in the core
A synthetic diagnostic was developed to better understand the relationship between Er and V|| predicted by PENTA and the velocities seen by each view
In the Core Flow Direction Changes Across the Beam/View Intersection Volumes

## Slide 28
Er measured by CHERS is ~5kV/m larger than the predicted Er profile in the outer half of the plasma
Er larger than the calculated values were also measured using probes [See Poster R. Wilcox on Thursday]
The predicted V|| does not change direction in the regions where Er is negative because of the positive diamagnetic flow
DKES and PENTA Predict Low Er for r/a>0.5, Total Flow Determined by Diamagnetic Flow
PENTA
Measured
DKES
Measured and Calculated Er
-
Er
Drive Terms

## Slide 29
Measurements made at 10 radial locations from 2 different viewing directions ( and
The direction of is used as the third constraint on the flow vector
The average local flow velocity is found from the flows measured by the two views and the geometric constraints
Two Viewing Angles Needed To Find Flow Direction
“Poloidal”
Views
“Toroidal”
Views
Three Constraints Used to Determine the Local Flow Speed and Direction:

## Slide 30
The Flow Perpendicular to the Magnetic Field Changes Speed and Direction in View Volume
changes direction and magnitude within the beam/view intersection volumes
The radial extent of the region predicted to have large will depend on which root exists in the multi-root region
Neutral
beam width
View
Electron root
chosen in multi-root region
Ion root chosen in multi-root region
km/s
Flow
Direction

## Slide 31
Electron root
chosen in multi-root region
The Flow Along the Magnetic Field is Dominated by the Pfirsch-Schlüter Flow For Electron Root Er
In the multi-root region the smaller, ion root, Er produces a larger net V||
When the electron root is chosen the Pfirsch-Schlüter flow, which changes direction across the “toroidal” views dominates the total V||
Neutral
beam width
View
Ion root chosen in multi-root region
km/s
Flow
Direction

## Slide 32
The velocity that would have been measured by each view for a given profile is calculated using the synthetic diagnostic
In the core the measured velocity is more than 20km/s less than that predicted by PENTA when either the electron or ion root is chosen where both are predicted
VthH+~100km/s; VthC+6~30km/s
Synthetic Diagnostic Shows Flows Predicted by PENTA Larger Than Measured Flows for r/a<0.5
Electron root
Ion root
Measured
Velocity Seen By
“Poloidal” Views
Velocity Seen By
“Toroidal” Views

## Slide 33
Neoclassical electron and ion fluxes are non-linear independent functions of radial electric field
Turbulent fluxes are assumed to be ambipolar
In steady state the radial electric field is determined by enforcing ambipolarity
Neoclassical Fluxes Are Not Intrinsically Ambi-Polar in Non-Symmetric Configurations

## Slide 34: Motivation
Flows improve plasma confinement and stability by
  Healing vacuum islands in stellarators
  Stabilizing resistive wall and tearing modes
Using neutral beams to drive flows is impractical for larger devices, intrinsic flows become important
Non-symmetric magnetic field components damp flows, but can in some cases increase flow drive
  Symmetry breaking terms are being added to tokamaks
  Non-symmetric fields in stellarators determine Er, but damp large flows
  HSX’s direction of symmetry allows for large flows