## Slide 1
1) For equivalent ECRH power, off-axis heating
results in lower stored energy and lower core
temperature
2) Plasma flow is significantly reduced with
off-axis heating. Doppler shift cannot account
for change in frequency or amplitude of density
fluctuations
3) Increased core density fluctuations with off-axis
heating ; may act to degrade energy confinement
Provides measure of
density gradient fluctuations
Core Density Fluctuation Measurements by Interferometry in the HSX Stellarator
Abstract
C. Deng , D.L. Brower, University of California, Los Angeles,
D.T. Anderson, F.S.B. Anderson, A. Briesemeister, K. Likin, J. Lore, J. Schmitt, J.N. Talmadge, R. Wilcox, K. Zhai, University of Wisconsin-Madison
HSX – Quasi-Helically Symmetry Stellarator
Interferometry System
53rd Annual Meeting of the Division of Plasma Physics, November 14-18, 2011, Salt Lake City, Utah
Coherent and Broad Band Fluctuation Measured by Far-Forward Scattering
major radius: 1.2 m
minor radius: 0.15 m
magnetic field: 1 T;
ECRH: 28 GHz ,
<150 kW
pulse length: < 50 ms
QHS
HSX Provides Access to Configurations With and Without Symmetry
QHS: helical axis of symmetry in |B|
Red|B|1.0 T
Blue|B|<1.0 T
Mirror
Flux Surface and Chord Positions
Mirror: quasi-helical symmetry broken by adding a mirror field
Coherent mode in QHS Plasma
Results From Three Techniques
Density Fluctuations Increase with off-axis Heating (QHS plasma, Bt=1T in CCW)
Plasma Parameter Time Traces
Plasma Parameters
Coherent mode observed in Mirror Plasma for BT=1 T (ccw)
Mode observed in density, not in magnetic signals
Density window for mode is narrow: (3.8-4.5)* 1012 cm-3
Decrease in ECE emission suggests decrease in energetic electron confinement
mode amplitude is higher on high field side
p phase shift observed across magnetic axis (m is odd)
mode not observed on external magnetic coils
Coherent mode in biased QHS plasma with Vbias=+300V
1. Interferometry, Differential Interferometry and Far-forward Scattering are used to measure density fluctuations in HSX
- line-integrated measurements, some spatial information
available by comparing chords
- differential interferometry is used to obtain core localized
measurements
2. Both coherent modes and broadband fluctuations are observed
3. For QHS plasma
- Significant changes (amplitude and frequency) of fluctuations
are observed when heating location changes from on-axis
heating to HFS heating
- Density fluctuation amplitude and frequency decrease with
of electron temperature
- core density fluctuations increase and confinement degrades
with off-axis heating
- coherent mode observed on density and magnetic when
heating slightly off-axis
4. Mirror plasma:
- Coherent mode observed on density fluctuation signal only,
- mode not sensitive to ECRH location
Future work will focus on identification of fluctuations
Measurement Techniques
1. Interferometry (phase measurement)
2. Far-Forward Collective scattering
(a) collective scattering within the
divergence of the beam
(b) amplitude measurement
3. Differential Inteferometry
The multichannel interferometer system on the HSX stellarator is optimized to measure electron density fluctuations by utilizing both phase and amplitude techniques Information on core and edge fluctuations can be realized by comparing chords at different locations or by use of the differential interferometry approach. Both coherent modes and broadband density fluctuations with frequency up to 250 kHz are measured. For quasi-helically symmetric plasmas with BT=1.0 T, significant changes (both amplitude and frequency) in the turbulent density fluctuation spectrum are observed when heating location changes from on-axis to high field side. Density fluctuation amplitude and frequency decrease with increasing of ECRH power (Te). Changes in fluctuations will be compared with measurements of plasma flow (by CHERS) as well as electron density and temperature profile modifications. When HSX is operated without quasi-helical symmetry at BT=1T and ne= 4x1012 cm-3, a coherent electrostatic mode at 28 kHz is observed. Fluctuation sensitivity to changes of heating location and ECRH power were not observed for these plasmas.
QHS: helical bands of constant |B|
Mirror: helical bands are broken
Localized Density Fluctuation Gradient Measurement
(1) For density gradient and gradient fluctuations
[differential interferometry]
(2) For density fluctuations (m=1) [standard interferometry]
Z
Plasma Conditions:
BT=1T, Counter Clockwise, QHS
Main Field Current IB=10891A
ne=4x1012cm-3 , PECRH=50kW
Scattering measurements
R-Ro=1.0 cm
1. Broadband fluctuations
2. Coherent mode at 16 kHz (stronger on neg. side)
3. Coherent mode observed on magnetic coils
Interferometer and Far-Forward Scattering Show Similar Results
Far-Forward Scattering
Interferometry
Density Fluctuations from Differential Interferometry Measurement
Directly measures phase
difference between
adjacent chords
[R-Ro: +1 and -0.5 cm]:
Coherence between two chords
Lower noise level and core localization for differential interferometer measurement
on axis heating:
IB=11000A
off axis heating:
IB=10600A
Core localized measurement of Density gradient fluctuations shows large increase in amplitude for off-axis heating
Significant change in density fluctuations with heating location for central chords
No change in density fluctuations with heating location for edge chord chords
Coherence between two adjacent central chords
Doppler shift (reduced) cannot account for higher frequency density fluctuations with off-axis ECRH
Electron Temperature and Density Profiles
Te (Thomson Scattering)
ne (Interferometer)
Very peaked Te profile flat or slightly hollow density profile (dTe/dr driven diffusion) negative density gradient reduction of density fluctuations
Coherent mode in Mirror Plasma
Coherent mode (density fluctuation) is observed for slightly inboard heating
Magnetic fluctuations observed on some Mirnov coils
ECE signals reduced when coherent mode present
No change in ne(r)
BT=1T in CCW direction
Frequency Spectrum of Density Fluctuations
Density fluctuations
Density gradient
fluctuations
No changes for broad band fluctuations
coherent mode was observed for slightly inboard heating
Amplitude and Phase of the Coherent Mode
Density mode amplitude peaked near plasma edge
Density shows p phase shift across magnetic axis; m is odd
Weak Magnetic fluctuations, external coils suggest m=1
Differences in coherent mode for Mirror and QHS configurations:
Mirror: density fluctuation only; QHS: both density and magnetic fluctuation
Mirror: sensitive to equilibrium density; QHS is not
Mirror: sensitive to direction of B field [cw or ccw]; QHS is not
Mirror: not sensitive to IB (heating location); QHS case is very sensitive to IB
Coherent mode observed in Biased QHS Plasma, and while broad band fluctuations did not change
Mode observed in both density, and magnetic signals
Amplitude and Phase
Plasma flow reduced for Off-Axis Heating Case
Input ECH power are similar, but significantly lower stored energy for off-axis heated plasma. Measured density fluctuations are of larger amplitude and at higher frequency for off-axis heating.
Interferometer System:
1. 9 chords
2. 1 MHz bandwidth
3. 1.5 cm chord spacing, width
k^ < 2 cm-1
Density fluctuations can be measured from information of:
Amplitude
Phase
Differential
Amplitude
Phase
Summary and Future Plans
Frequency Spectrum
No Significant Change in Density Profile
Frequency Spectrum
Density Profile