## Slide 1
Laser Blow-Off Impurity Injection Experiments in the HSX Stellarator
C. Clark1, D.T. Anderson1, F.S.B Anderson1, K. Likin1, J.N. Talmadge1, K. Zhai1, J. Lore2,
1HSX Plasma Laboratory, Univ. of Wisconsin, Madison, USA, 2 Oak Ridge National Lab, Oak Ridge, TN
Overview and Motivation
Impurity control and effective helium exhaust are open areas of research for the stellarator reactor concept
  The expected “Ion Root” operating point of a stellarator reactor is predicted to enhance impurity confinement
  Some stellarators have seen unexpected, and unexplained increase in impurity transport under specific operating conditions
    W7-AS had an “High Density H-mode”[Grigull, ’01]
    LHD has an impurity “hole” [Ida, ‘09]
  No clear path exists to satisfactory impurity handling in a reactor scale stellarator
We have undertaken an experimental program to measure the impurity transport properties of the HSX stellarator. Our goals are to:
  Inject aluminum neutrals into HSX plasmas using a laser blow-off technique
  Measure the resulting radiation using AXUV photodiode arrays
  Determine the impurity diffusivity and convective velocity using the STRAHL code
  Compare these findings with the neoclassical model using the PENTA code
Progress has been made toward the experimental goals
  Aluminum has been injected into HSX discharges
    The injection was visible on a photodiode
    The injection did not perturbing the background plasma parameters
  Two photodiode pinhole cameras have been installed on HSX, and five more are under construction.
Laser Blow-Off
Calculating Transport Coefficients with STRAHL
Initial Results:
Simulation of Impurity Radiation Profiles:
Reconstruction of Impurity Emissivity Profile
Determining the View of Each Detector:
Synthetic Diagnostic with Noisy Data:
The volume around the paraxial ray is discretized
The solid angle of the detector, as viewed from the center of each volume element, is calculated
  This gives the relationship between the emission in each volume element and the signal at the detector
Since each volume element is small, it is taken to be located at a single radial location
  The volume elements can be binned into the appropriate portion of a matrix relating the 1D emissivity profile to the power incident on each detector
Exact expected signals are calculated for each detector from the view information and the emissivity profile
A Monte-Carlo code adds uncorrelated noise (5% std. dev.) to the exact signal predicted for each detector
  At each iteration, a least-squares inversion is performed
The mean and standard deviation of the inversion results are compared to the exact profile
Impurity radiation will be detected with AXUV photodiode arrays
  Two have been installed on HSX
  Five more are under construction
The detectors view the plasma through a 1 mm pinhole to achieve spatial resolution
A beryllium filter can be rotated over the pinhole on several of the detectors so that the photodiode detects only the soft X-ray emission
Exact Profile
HSX Beam Line Details:
Laser: 850 mJ YAG – Surelight III
  Allows use of up to a 4 mm spot at 7 J/cm2
Solid angle of injection: 3 x 10-3 sr
Spot size adjustable by movable lens
Projected to inject up to 1016 neutrals into the plasma per pulse
Comparison of exact emissivity profile and inversion results
Mean Inversion Results
A laser blow-off target that has been used on HSX
Test injections have been performed with:
  1 μm aluminum layer
  Full laser power (850 mJ)
  1 mm diameter laser spot
The injections were visible on photodiode
They did not significantly impact the line-averaged density or stored energy
Total Emissivity Profile
Soft X-Ray Emissivity Profile
Assumes nAl = 0.01 ne
Total emissivity was calculated with ADAS, using HSX plasma parameters
  Integrated: PTot = 1.65 kW
The portion of the radiation that would transmit through a 5 μm beryllium filter was also calculated
  Integrated: PSXR = 10 W
  SXR data won’t be useful in the outer two-thirds of the plasma
Standard Deviation of Inversion Results
Detector Signals
With Noise Added
Inversion
AXUV-20EL Chip
Pinhole
Channel 1 View
Channel 20 View
Separatrix
Vessel
Laser
Metal
Glass Slide
Laser Firing Time
The HSX Laser Blow-Off System
The neutral spectrum for a 2 μm aluminum film illuminated with a 7 J/cm2 laser pulse [Breton ‘80]
Bare Photodiode
Background Parameters
Simulation of Laser Blow-Off
Simulation of Impurity Beam Penetration:
A schematic view of the laser blow-off process
Neutral Penetration Prediction
Background Plasma Parameters
Considers only electron impact ionization
  Atomic data from ADAS
Neutral spectrum taken from [Breton ‘80]
Projects adequate deposition within the confinement volume
Last Closed Flux Surface
A glass slide with a 0.5–2.0 μm thick layer of the selected material is back-illuminated with a laser
  This creates short burst of neutrals, which ballistically enter the plasma
  The energy spectrum of neutrals is a function of the laser energy density, film thickness, and material
  The number of neutrals injected can be controlled with spot size and film thickness
The laser blow-off properties of aluminum have been particularly well characterized by other researchers [Marmar, ’75 & Breton, ’80]
The transport code STRAHL [Behringer, ‘87] is used to solve the 1-D continuity equation for each impurity charge state, including the source / sink term due to ionization / recombination from adjacent charge states
ADAS is used for atomic data calculations
The background plasma parameters are assumed to be constant and are inputs to the code
Temporal and spatial impurity source rates, diffusivities and convective velocities are inputs to the code
The code outputs the time dependent emissivity profile
When used in conjunction with a nonlinear optimization algorithm, STRAHL can be used to determine the impurity convective velocity and diffusivity from the time dependent emissivity