## Slide 1
Plasma Pressure / B•J Contours
Poloidal dimension
Radial dimension
Toroidal Angle (rad)
Poloidal Angle (rad)
HSX Magnetic Field Strength
Field Line
Magnetic Field Ripple
Density Fluctuation Spectrum
Forward Scattering Data
Mirror
QHS
Reflectometer Data
Frequency [kHz]
PSD [a.u.]
Time Evolution of Itor
Bq in Poloidal Plane
V3FIT
@ t = 8 ms
t = 50 ms
Total bi-coherence of Eq
Parallel Velocity Profile
Overview of HSX Stellarator Experiments
K. M. Likin, D.T. Anderson, F.S.B. Anderson, A.R. Briesemeister, D.L. Brower1, C.A. Clark, C.R. Cook, C. Deng1, J.W. Radder, J. C. Schmitt, J.N. Talmadge, G.M. Weir, R.S. Wilcox, K. Zhai
HSX Plasma Laboratory, Univ. of Wisconsin, Madison, WI, USA; 1University of California, Los Angeles, CA, USA
Summary
Density Fluctuations
In HSX, density fluctuation spectrum is measured by the interferometer (forward scattering) and the reflectometer
Density fluctuation spectrum in QHS and Mirror are almost identical except a narrow feature at 28 kHz; Te profile in QHS is peaked with central temperature ~ 1.2 keV and Mirror plasma with core Te ~ 500 eV does not manifest a steep Te gradient
Second ECRH System and ECE
Second ECRH system is to be operational early next year; second gyrotron has been tested on a dummy load; assembly of the second transmission line is expected to complete in this December
Additional 200 kW will be available
To shift the ITB region the steerable mirror is designed for off-axis heating
To study an electron diffusivity the second heating source can produce a power modulation in a heat pulse propagation experiment
1-D modeling of Te perturbations in HSX plasma has been made
Next steps on ECE diagnostic: (1) to improve sensitivity of some ECE channels; (2) to model ECE signals from the modeled Te perturbation
Parallel Velocity and Er
Large parallel flow (~15 km/s) observed for QHS configuration, often neglected in neoclassical calculations
Non-momentum conserving calculations under-predict V|| by an order of magnitude compared to measured values
Derived radial electric field corresponds to that in the neoclassical ion root regime
Equilibrium Reconstruction
Impurity Transport
About 1% of aluminum will be injected into plasma by a laser blow-off technique
Time evolution of the Al+ radiation will be measured by a set of bolometers and SXR detector arrays
Impurity diffusivity and convective velocity will be found with the STRAHL code and a nonlinear optimization algorithm
Thomson Scattering diagnostic is being upgraded to get three snapshots of plasma profiles in each discharge
See poster by Alexis Briesemeister
The steady-state neoclassical bootstrap current is calculated by PENTA and the evolving current profile is modeled by a diffusion equation with a 3D susceptance matrix
Toroidal current matches or exceeds the neoclassical ion-root solution for most cases
A set of small coils outside the HSX vessel provide data for 3-D equilibrium reconstruction and current profile by the V3FIT code
At the beginning the dipole-field from the Pfirsch-Schlüter current is detected ; later a contribution from the bootstrap current is measured as well
Zonal Flow
Zonal flow levels predicted to be higher in configurations optimized for reduced neoclassical transport
A presence of zonal flow can be found through the wave coupling; high bi-coherence indicates three waves interaction into a plasma
In HSX, high bi-coherence and long-range correlations of potential fluctuations in the region of the induced radial electric field are consistent with zonal flow formation
Major radius of equivalent torus - 1.2 m
Averaged minor plasma radius - 0.12 m
Magnetic field on plasma axis - up to 1.1 T
Rotational transform - 1.05 (axis) => 1.12 (edge)
ECRH power from one source - up to 100 kW
Total number of coils - 96
48 Modular coils produce the quasi-helically symmetric (QHS) magnetic configuration
There is almost no toroidal curvature in the QHS configuration that with a high effective transform (ιeff ~ 3) results in small banana widths, low plasma currents and low neoclassical transport
48 Planar coils can alter the main configuration to degrade the QHS symmetry increasing magnetic field ripple, viscous damping and neoclassical transport to a higher level. Magnetic configuration with a broken symmetry is called Mirror
Conventional Stellarators
At 100 kW of launched power the central electron temperature in QHS is above 2 keV while in Mirror mode the maximum Te value does not exceed 1.4 keV; this results is, primarily, due to better confinement in QHS than in Mirror
Emphasis now is investigating anomalous and neoclassical electron transport by heating electrons to low collisionality regime at higher power level; the second ECRH system will be available shortly
Momentum conservation between species must be taken in account to predict the parallel velocity in HSX measured by CHERS diagnostic
When a bias is applied to the plasma, a signature of zonal flow has been detected in HSX
V3FIT code used for plasma equilibrium reconstruction predicts a broad pressure profile
Measured toroidal current matches the estimated value by PENTA code with Er that corresponds to the neoclassical ion root solution
Impurity transport is a key issue for stellarators; HSX is starting an investigation using a laser blow-off technique with bolometry and soft X-ray diagnostics
We use VMEC, PENTA, GNET, SIESTA codes to model the HSX experiment
r/ap
Te (keV)
r/ap
r/ap
ne (1018 m-3)
Pabs (W/cm3)
Absorbed Power Profile
Electron Temperature and Density from TS diagnostic
See poster by John Schmitt
See poster by Robert Wilcox
See posters by Chris Clark and Kan Zhai
See poster by Gavin Wier
See poster by Chuanbao Deng
See poster by Carson Cook
Equilibrium with Islands
Using SIESTA, equilibrium can be resolved in finite-beta plasmas; the code also will be used for optimization of 3-D magnetic configurations
Due to the strong helical shaping in HSX, a large number of modes and pseudo-spectral points are required within SIESTA
w/in Deposition region 1
w/in Deposition region 3
w/in Deposition region 2
New Launching Antenna
Steerable mirror
Laser Blow-off Diagnostic
Laser beam
Target inside chamber
HSX valve
HSX Device