## Slide 1: Measurement, Reconstruction and Modeling of Equilibrium Currents in the HSX Stellarator
J.C. Schmitt, J.N.Talmadge, J.Lore
15TH WORKSHOP ON MHD STABILITY CONTROL
15-17 November, 2010 Madison, WI

## Slide 2: Toroidal current is predominantly bootstrap-driven
Electron Cyclotron Resonance Heating
  1st Harmonic Ordinary-mode
  Perpendicular launch
No ohmic drive
Toroidal current reverses with B-field direction
Bootstrap current induces toroidal current with long decay times: τη||/μ0 ≥ τEXP
50 kW ECH
Net Toroidal Plasma Current
BCCW
BCW
Ne = 3
ρECRH = +0.18 (OB)

## Slide 3: Equilibrium Currents with Quasi-Helical Symmetry
Pfirsch-Schlüter current rotates with the |B| contours.
Bootstrap current is in the opposite direction and reduced compared to a tokamak.
The evolving current profile is modeled with a diffusion equation using a 3D susceptance matrix.
V3FIT calculates the expected signal response for an array of magnetic diagnostics.
V3FIT reconstructs the pressure and current profiles based on the magnetic diagnostics signals.

## Slide 4: Bootstrap current depends on Er
Te, Ne from Thomson Scattering.
Ti from ChERS. Zeff ≈ 1 from Bremsstrahlung radiation (ChERS optics).
PENTA1 calculates the fluxes. Er is determined by ambipolarity.
The electron-root reverses the direction of the bootstrap current.
1 D.A. Spong, Phys. Plasmas 12, 056114 (2005).
Ne
Te
Ti
JBS e-root
JBS i-root
Multiple ambipolar solutions

## Slide 5: Toroidal current evolves during shot
50 kW ECH
-60 A
-364 A
If electron-root dominates: IBS = -60 A If ion-root dominates: IBS = -364 A
The measured net current is between the predicted limits of the ion- and e-roots.
The extrapolated steady state value is -345 A. τL/R ~ 40ms.
∆IBS = 304 Amps
JBS e-root
JBS i-root

## Slide 6: Modeling the Evolution of the Toroidal Current
3D susceptance matrix links toroidal and poloidal currents and magnetic fluxes2
  S12 = S21 = 0 for Tokamaks
  S11 ≈ S12 ≈ S21 for HSX
1-D diffusion equation for rotational transform
Boundary conditions
  Finite current density on axis:
  iota @ LCFS set by measurement:
Any non-inductive source
  2 P. I. Strand and W. A. Houlberg, Phys. Plasmas 8, 2782 (2001).

## Slide 7: V3FIT3 Calculates the Magnetic Diagnostics Signals
3 Nucl. Fusion 49 (2009) 075031.
Φ=1/2 Field Period
Φ=0 (symmetry plane)
Diagnostic set includes two Rogowski coils, two flux loops , 32 dB/dt sensors and the limiter location.
VMEC is the equilibrium solver. The plasma pressure, toroidal current profile and net toroidal flux are specified with up to 9 free parameters.
For reconstruction, V3FIT adjusts the parameters to minimize the difference between the measured and modeled signals.
Thanks to James Hanson and Steve Knowlton for the assistance in using V3FIT

## Slide 8: The Pfirsch-Schlüter current rotates helically
The plasma pressure profile is calculated and used in V3FIT to find the magnetic response due to the Pfirsch-Schlüter current.
The net toroidal current is set to 0.
Red Contours: JPS OUT OF PLANE
Blue Contours: JPS IN TO PLANE
Φ≈ 1/6 Field Period
Φ≈1/2 Field Period
8
Poloidal Index
16
1
17
32
18
25
26
4
12
Bθ
Br

## Slide 9: A ‘dipole-like’ response is predicted for the case of no net toroidal current
Bθ
Bθ
Br
Br
≈ 1/2 FP
≈ 1/6 FP
Φ≈ 1/6 Field Period
Φ≈1/2 Field Period
8
Poloidal Index
16
1
17
32
18
25
26
4
12
Bθ
Br
The sign of the signals at the two toroidal locations demonstrate a phase shift showing the helical rotation.
Poloidal Index
Poloidal Index

## Slide 10: Bootstrap Current Contributes Little to Br Early in Shot
P.S. only
The toroidal current profile is simulated in time and the diagnostic response is predicted with V3FIT.
A small net toroidal current (40 A) contributes to the Bθ component.
tsim=8 ms
Bθ
Bθ
Br
Br
≈ 1/2 FP
≈ 1/6 FP
Poloidal Index
Poloidal Index

## Slide 11: Confirmation of the Helical Rotation of the Pfirsch-Schlüter Current
The experimental signals at t=8ms agree well with theory in terms of the sign and phase.
Good agreement in magnitude. Reconstruction with V3FIT may resolve the differences.
tsim=8 ms
P.S. only
Bθ
Bθ
Br
Br
≈ 1/2 FP
≈ 1/6 FP
Poloidal Index
Poloidal Index
P.S. only
tsim=8 ms

## Slide 12: Later in Time, the Largest Signals are from Bootstrap Current
Simulated profiles at 25ms and 50ms.
Bθ has large unidirectional contribution from <J∙B>.
Br is dominated by the m=2 structure of the vacuum vessel.
Bθ
Bθ
Poloidal Index
Poloidal Index
Br
Br
50 ms
25 ms

## Slide 13: Measured signals are close to the simulated ones
Measurement evolves slightly faster than simulated values.
Possible sources of error: Zeff, initial plasma profiles, neoclassical calculation of bootstrap current.
The pressure profile and evolved current profile serve as an ‘initial guess’ in the V3FIT reconstruction attempt.
Poloidal Index
Poloidal Index
50 ms
50 ms
Bθ
Bθ
Br
Br

## Slide 14: The reconstruction minimizes the mismatch between the measured and modeled signals
Initial guess in blue
Pressure profile becomes wider; Current density is shifted radially outward.
Posterior sigmas are large: Need to reduce the # of free parameters in the model.
Poloidal Index
Poloidal Index
50 ms
50 ms
Bθ
Bθ
Br
Br
Reconstruction in red

## Slide 15: Toroidal Currents with Quasi-Helical Symmetry
The direction of the bootstrap current is reversed and reduced by ~1/3 compared to an equivalent tokamak (same iota, Rmajor, rminor). This results in a reduction in rotational transform.
The Pfirsch-Schlüter current rotates with |B| contours and is reduced by ~1/3 compared to a tokamak, demonstrating the lack of toroidal curvature.
The evolving current profile is modeled with a diffusion equation using a 3D susceptance matrix. Expected magnetic diagnostic signal are calculated with V3FIT.
Continue to improve the V3FIT reconstruction. e.g., Reduce the # of free parameters in the reconstruction to achieve reasonable uncertainties in the profiles.